## Slide 1
Automotive Electronics & AUTOSAR with Topology
GROUP 5

## Slide 2
What is Automotive Electronics?
Automotive electronics include ECUs, sensors, actuators, and controllers used to manage engine performance, braking, infotainment, and safety systems.
Key Components of Automotive Electronics
Electronic Control Units (ECUs)
Sensors (speed, temperature, position)
Actuators (motors, valves)
Communication Buses (CAN, LIN, Flex Ray)
Power Supply (battery, alternator)
EXPLAINED BY:- SUMMA

## Slide 3
Automotive Electronics - Detailed Components
Electronic Control Units (ECUs)
Function: ECUs are the "brains" of the vehicle's electronic systems, processing sensor inputs and sending commands to actuators. Each is programmed for specific tasks.
Examples: Engine Control Unit (ECU/ECM), Transmission Control Unit (TCU), Body Control Module (BCM), Anti-lock Braking System (ABS) module, Airbag Control Unit (ACU).
Sensors
Function: Detect and measure physical quantities (e.g., speed, temperature, position), converting them into electrical signals for ECUs.
Examples: Wheel speed sensors, engine coolant temperature sensors, throttle position sensors, crankshaft position sensors, oxygen sensors.
EXPLAINED BY:- SUMMA

## Slide 4
Actuators & Communication Buses
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Actuators
Function: Receive commands from ECUs and convert electrical signals into physical action.
Examples: Electric motors (power windows), solenoid valves (ABS systems), fuel injectors, ignition coils.
Communication Buses
Function: Networks within the vehicle enabling ECUs to communicate and exchange data efficiently.
Common Types:
  CAN (Controller Area Network): Robust, widely used for safety-critical systems (engine, braking).
  LIN (Local Interconnect Network): Simpler, lower-cost for non-critical applications (windows, mirrors).
  Flex Ray: High-speed, fault-tolerant for advanced applications (drive-by-wire).
  Automotive Ethernet: Increasingly used for high-bandwidth ADAS and infotainment.
  EXPLAINED BY:- USHA

## Slide 5
Real-Life Example: ABS (Anti-lock Braking System)
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Real-Life Example: ABS (Anti-lock Braking System)
Sensors detect wheel lock: Wheel speed sensors monitor rotational speed and detect if wheels lock up during hard braking.
ECU calculates response: The ABS ECU processes sensor data and determines necessary brake pressure adjustments.
Actuator modulates brake pressure: The ABS ECU sends commands to hydraulic actuators (solenoid valves) to rapidly adjust brake pressure to individual wheels.
Prevents skidding and improves stability: By preventing wheel lock, ABS maintains steering control and vehicle stability during emergency braking.
EXPLAINED BY:- USHA

## Slide 6
What is AUTOSAR?
What is AUTOSAR?
AUTOSAR stands for Automotive Open System Architecture.
It is a standard software framework that promotes software reuse, scalability, and interoperability.
AUTOSAR Architecture Layers
Application Layer: Contains vehicle functions
RTE (Run-Time Environment): Manages communication
Basic Software (BSW): Provides common services
MCAL: Interfaces with microcontroller
EXPLAINED BY:- PRINCE

## Slide 7
AUTOSAR Architecture Layers
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Application Layer
Function: Highest layer containing vehicle functions and application logic. Software components are independent of hardware.
Example: Cruise control logic, engine management functions, navigation UI.
RTE (Run-Time Environment)
Function: Acts as a virtual communication bus and abstraction layer between Application and BSW. Manages inter-component and inter-ECU communication.
EXPLAINED BY:- PRINCE

## Slide 8
AUTOSAR Architecture Layers - BSW & MCAL
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Basic Software (BSW)
Function: Provides common, standardized services independent of application but dependent on the microcontroller.
Includes: Modules for communication, memory management, I/O, operating system services, diagnostics.
Sub-layers: Services Layer, ECU Abstraction Layer (EAL), Complex Device Drivers (CDD).
MCAL (Microcontroller Abstraction Layer)
Function: Lowest software layer, directly interfaces with microcontroller hardware. Provides a standardized API for peripherals.
Example: Drivers for GPIOs, ADC, PWM, CAN controller.
EXPLAINED BY:-DEEPAK

## Slide 9
Benefits of AUTOSAR
Benefits of AUTOSAR
Reusability: Enables software components to be reused across projects and vehicle lines, reducing development effort.
Safety: Provides mechanisms for developing safety-critical software, adhering to standards like ISO 26262.
Cost Efficiency: Reduces software development, testing, and maintenance costs.
Vendor Independence: Allows OEMs to source components from different suppliers for seamless integration.
Scalability: Supports a range of ECUs from simple to high-performance.
Interoperability: Ensures components from various suppliers work together effectively.
EXPLAINED BY:-DEEPAK

## Slide 10: Topology in Automotive Electronics
Topology in Automotive Electronics
Topology defines the arrangement of ECUs and communication.
It impacts communication efficiency, reliability, and cost.
Common types:
Bus Topology
Star Topology
Ring Topology
EXPLAINED BY:-JYOTISMAN KIRTI PRAKASH

## Slide 11: Bus Topology
Bus Topology
Description: All devices share a common communication line (e.g., CAN Bus). Data is broadcast.
Advantages:
  Simple
  Low-cost
Disadvantages:
  Single point of failure (if main line breaks)
  Limited bandwidth (shared medium)
  Difficult troubleshooting.
Typical Automotive Use: Widely used for CAN bus networks (powertrain, chassis, body).
EXPLAINED BY:-JYOTISMAN KIRTI PRAKASH

## Slide 12: Star Topology
Star Topology
Description: All nodes connected to a central hub (e.g., used in Ethernet-based systems). Communication passes through the hub.
Advantages:
  Improved reliability (failure in one connection affects only that node).
  Easier troubleshooting.
  High bandwidth potential (dedicated connections).
  Easily scalable.
Disadvantages:
  Central point of failure (if hub fails, entire network fails).
  More cabling, higher cost.
Typical Automotive Use: Preferred for high-speed networks like Automotive Ethernet (infotainment, ADAS).
EXPLAINED BY:-VIKAS

## Slide 13: Ring Topology
Ring Topology
Description: Devices connected in a closed loop. Data travels sequentially around the ring.
Advantages:
  Ordered access (prevents collisions).
  Can support high data rates.
  Redundancy with dual rings (data can travel in opposite direction if one part fails).
Disadvantages:
  Single point of failure in a simple ring.
  Complex troubleshooting.
  Adding/removing devices disrupts the network.
Typical Automotive Use: Less common as primary general-purpose network; sometimes in specific fault-tolerant sub-systems.
EXPLAINED BY:-VIKAS

## Slide 14
THANK YOU